The Programming Language "immediate C"

John E. Wulff, B.E., M. Eng. Sc.
john@je-wulff.de

# 0. Abstract
immediate C - iC for short - is an extension of the language C. It utilizes the syntax of C to give meaning to statements that have no semantic support in C. In addition to standard variables, which are modified by the flow of instructions, iC provides so called 'immediate' variables, whose values are updated, whenever a change of input calls for an immediate change in output. An efficient Data Flow technique implements this strategy.
iC provides programmers with built in operators, whose function is closely modelled on integrated circuits. The name iC is a reminder of this fact. Logical AND, OR and NOT as well as D flip flops, SR flip flops and many others are implemented in such a way, that their use follows the same design rules, which apply to their hardware counterparts. These rules have led to a well-developed hardware technology, whose effectiveness is demonstrated by the success of today's complex computer hardware. Particularly the concept of clocked functions plays an important role in iC. It gives the same protection against timing races in iC programs, as it provides for hardware IC designs.
Writing programs in the language iC has the added quality, that many simple ideas and relationships, which should result in direct actions, can be written down immediately in one line. The coding of call back routines and other overhead is not required. It was this thought, which also prompted the name "immediate C".

# Zusammenfassung
immediate C - kurz iC - ist eine Erweiterung der Sprache C. Sie basiert auf der Syntax von C und gibt vielen Befehlen Bedeutung, die keine semantische Unterstützung in C haben. Zu den einfachen Variablen, die im normalen Programmfluss verändert werden, kommen in iC so gennante 'immediate' oder 'sofort' Variablen, dessen Wert sofort verändert wird, wenn eine Eingangsänderung, die sofortige Änderung eines Ausgangs zur Folge hat. Um dies zu erreichen, wird eine effiziente Datenfluss-Technik eingesetzt.
iC stellt Programmierern eingebaute Operatoren zur Verfügung, deren Arbeitsweise die Funktionen von IC-Bausteinen modelliert. Der Name iC soll an diese Tatsache erinnern. Logisches UND, ODER und NICHT sowie D flip flops, SR flip flops und viele mehr sind so implementiert, dass deren Anwendung den gleichen Entwurfsregeln entspricht, wie die der entsprechenden IC-Bausteine. Diese Regeln haben zu einer ausgereiften Technik geführt, deren Wirksamkeit durch unsere heutige komplexe Computertechnik belegt ist. Besonders das Konzept von getakteten (clocked) Funktionen spielt in iC eine wichtige Rolle. Damit wird derselbe Schutz gegen Laufzeit-Probleme erreicht, der damit in IC-Schaltkreisen bewirkt wird.
Programme die in iC geschrieben werden, haben das zusätzliche Merkmal, dass viele einfache Ideen und Zusammenhänge, die zu direkten Aktionen führen sollen, sofort in einer Zeile niedergeschrieben werden können. Callback-Routinen sind nicht notwendig. Auch dieser Gedanke ist im Namen "immediate C" enthalten.
# Introduction
immediate C - iC for short - is an extension of the language C. It utilizes the syntax of C to give meaning to statements that have no semantic support in C. This methodology was originally used to develop C++ from C. In addition to standard variables, which are modified by the flow of instructions, iC provides so called 'immediate' variables, whose values are updated, whenever a change of input calls for an immediate change in output. An efficient Data Flow technique implements this strategy.
iC provides programmers with built in operators, whose function is closely modelled on integrated circuits. The name iC is a reminder of this fact. Logical AND, OR and NOT as well as D flip flops, SR flip flops and many others are implemented in such a way, that their use follows the same design rules, which apply to their hardware counterparts. These rules have led to a well-developed hardware technology, whose effectiveness is demonstrated by the success of today's complex computer hardware. Particularly the concept of clocked functions plays an important role in iC. It gives the same protection against timing races in iC programs, as it provides for hardware IC designs.
## Relationship to Object Orientation
immediate C uses the OO-paradigm in its concept. Each immediate variable is an independent object, which acts on other immediate variables by a number of methods. These methods are expressed in a number of functions and overloaded on to the logical and arithmetic operators. In conventional OO languages like Smalltalk or C++, a method is an action which acts on the object owning the method. Conceptually descriptions of Object Orientation talk of methods being actions or messages sent from one object to another. It is in this sense that iC immediate variable objects interact with each other by the use of Data Flow techniques.
## Relationship to Instruction Flow Languages
Traditional High Level Languages such as FORTRAN, Pascal or C are called Instruction Flow Languages, because they express instruction sequences for abstract machines, which are closely modelled on the underlying, instruction driven machine. By being independent of the actual machine, these languages have helped to hide unessential details of the hardware, to make programs portable and to focus the programmer's attention on the problem to be solved. The overwhelming usefulness of these instruction flow languages to express precise algorithms is recognized in iC, by including the whole of C or C++ as a subset, for dealing with algorithmic problems in established ways. Learning of the language iC should therefore be very easy for C and C++ programmers.
Many of the undesirable characteristics of the underlying hardware are reflected in today's High Level Languages. These characteristics make it difficult to express a large number of everyday problems briefly and clearly. Particularly the manipulation of events is not easy to integrate into programs written in traditional High Level Languages. Yet events play an increasing role in today's interactive, mouse driven programs. Many different functions must be ready to execute as a result of external or user generated events, which occur at unpredictable times. The instruction driven computer only executes a particular instruction, when the flow of instructions in a program gets around to executing that instruction. This statement may sound pedantic, but much of the complexity of modern programs is a direct result of this fundamental truism. How does one organize a program, so that it can respond quickly to many and varied external events? iC provides answers to this question.
The interrupt mechanism, designed to tackle such problems at a system level, is intractable for the average programmer and is not supported in a general way by most High Level Languages. iC harnesses interrupts and hides their complexity.
## Programmable Logic Controllers
The situation is even more critical in systems that deal with a large number of external inputs. In the early 1980's a completely new class of computer was developed to deal with such problems in the environment of factories and machine control. These are the "Programmable Logic Controllers" or "PLC" for short. (SPS or Speicher-Programmierbare Steuerung in German) Conventional PLC's have a standard instruction driven architecture. They differ from conventional computers in two main areas:
- They provide fast bit instructions and data access to individual bits on top of the more conventional instructions to manipulate data words.
- They have a built in operating system, which runs the stored program over and over. Inputs are automatically polled at reasonably short intervals and Boolean and arithmetic expressions making up the stored program are re-evaluated continuously. This is necessary, because outputs and intermediate values in a PLC are assumed to reflect an immediate transformation of the inputs, as carried out by the expressions of the stored program.
This organization of PLC's has two very serious drawbacks, which are direct consequences of the differences mentioned:
- Conventional PLC's require a special CPU, which can never be as cheap as a mass produced microprocessor chip, or they emulate the PLC instruction set, in which case they are slow.
- The cyclic execution of the stored program sets very real limits to the length of possible programs. The longer the program, the longer the cycle time, which is the time interval at which inputs are polled. If this time gets too long, the response of the PLC is no longer acceptable for many applications.
PLC's are facing a crisis on two fronts:
- Traditionally PLC program memories were measured in kilobytes. Today megabytes of memory are available at low cost. This 1000 fold increase in potential program size cannot be utilized with the cyclic execution strategy of conventional PLC's. Even with a 10 fold increase in speed, these machines would be too slow.
- The second crisis is the lack of a High Level Language for PLC's. Most PLC programs are developed with antiquated tools that support semi graphical languages for Boolean logic and assembly programming for numerical subsystems. The international standard IEC-1131 is attempting to fill this vacuum by specifying such a language. Unfortunately this standard simply freezes current programming practice, by incorporating five different languages, four of which are the semi graphical and assembly languages in common use today. For algorithmic programming it introduces a completely new High Level Language called 'Structured Text', which will require a large learning effort by programmers and whose utility in the limited area of PLC's seems doubtful. IEC-1131 makes no attempt to confront the fundamental speed problems facing PLC programmers.
Because PLC's are completely compute bound, the type of program organization they use is unacceptable for standard computers. Nevertheless many programmers designing event controlled applications on standard computers resort to polling schemes, despite the drawbacks involved. The High Level Languages they use do not give them any simple alternatives.
The language iC can be used to program standard computer systems and PLC's in a uniform way. iC is fast, because it responds immediately to any changes in input, and does not waste time evaluating expressions, whose input operands have not changed. The extensions which iC offers over the algorithmic language C, can also be coded graphically, using current CAD packages for IC design. For factory staff, who require very simple programming methods, the use of Ladder Diagram (LD) or Function Block Diagram (FBD) in conformity with IEC-1131, using suitable front ends is possible.
## Summary
Writing programs in the language iC has the added quality, that many simple ideas and relationships, which should result in direct actions, can be written down immediately in one line. The coding of call back routines and other overhead is not required. It was this thought, which also prompted the name "immediate C".
# Language description
## Immediate Variables
An immediate variable is a data object that has a value, but which also has the ability to transmit any change in its value as an event. This event triggers the re-calculation of all expressions that contain the immediate variable. The fundamental assumption is, that the value of an expression only changes, if one of the variables making up the expression changes. Thus it is only necessary to re-calculate an expression, if one of the variables making up the expression changes. Conversely, if an expression is re-calculated whenever one of its variables changes, and all unnecessary recalculations of expressions are left out, the value of all expressions will be up to date within a very short time. Immediate variables provide the mechanism to make this strategy possible.
iC introduces the type modifier imm to declare immediate variables of the basic data types int in C and the basic data type bit, which is a new data type in iC. There are also the data types imm clock and imm timer discussed later.
Type bit declares variables capable of holding the values 0 and 1. Unless the C or C++ compiler, used to translate the generated code, itself supports bit as a basic data type, the use of type bit is restricted to imm bit. The word boolean was avoided deliberately, because it has a different semantic bias in languages where it is used. (Truth of a test rather than single bit objects).
## Immediate Expressions
Immediate expressions are arithmetic or boolean expressions external to all functions, which contain at least one immediate variable. Immediate arithmetic expressions may also contain constant expressions. An immediate expression is re-calculated when one of the immediate variables it contains has changed. If an expression consists only of constants and no immediate variables it is a constant expression evaluated once during initialisation.
## Operators in immediate expressions
Most operators available in C may be used with immediate variables. The precedence of the operators is the same as in C. Some C operators ar not valid for immediate expressions, because the semantics are different. These are the increment and decrement operators ++ and --, as well as structure, array and pointer operators [ ] -> .(dot) &(address of) and *(pointer dereference). Assignment expressions += etc. are also not allowed. These restrictions do not apply to embedded C code in literal blocks and immediate if else or switch statements, which will be introduced later.
### Arithmetic and Relational Operators
The binary arithmetic operators + - * /, the modulo operator %, as well as unary - and + operate on numeric values and yield numeric results of type imm int. The same applies to the shift operators << and >>. If an operand of the wrong type is used with one of these operators, automatic type conversion takes place. Values of type imm bit are converted to the int values 0 or 1 corresponding to the values of the bit. The relational and equality operators <, <=, >, >=, ==, != also have numeric operands, but these operators yield imm bit results by default.
### Bitwise and Bit Operators
The operators &, |, ^ and ~ carry out bitwise manipulation on integer words – just like in C, if all the operands are of type imm int. The result is an imm int. Immediate arithmetic, relational and bitwise logical expressions with numeric operands may contain constants, as well as immediate operands.
The operators &, |, ^ and ~ carry out the bit manipulation operations and, or, exlusive-or and not on imm bit objects, if one of the operands is of type imm bit. The result is an imm bit. Any operands of type imm int are converted to imm bit. The numeric value 0 converts to 0 (false), any other arithmetic value converts to 1 (true). The bit operators are used frequently in immediate C, since bit manipulation is very common in event driven sytems – more so than in algorithmic programs written in conventional languages like C, which does not even provide a type bit. Such logical bit expressions in immediate C may not contain any constants or non-immediate values. Constants in immediate bit expressions do not make much sense. They either do not change a variable (a & 1, b | 0) or they produce another constant (c & 0, d | 1, ~1).
### Logical Operators
The logical connectives && and || are executed as arithmetic expressions, when one of the operands is of type imm int. Evaluation is from left to right, and evaluation stops when the truth or falsehood of the result is known – just like in C. The result is of type imm bit by default. The unary complement operator !, operating on an imm int produces an imm bit result.
The operators &&, || and ! with only imm bit operands are interpreted by the compiler exactly like the logical operators &, | and ~. There is little sense converting such bit operands to integers, evaluating the arithmetic expression and then converting back to a bit. Since evaluation of && and || in bit expressions is not from left to right as expected, but depends on which operands in the expression change, their use and the use of ! in expressions where all operands are imm bit is deprecated and causes a warning.
### Conditional Expressions
The operators ? : implement conditional expressions, which are evaluated as a whole in an arithmetic context. The conditional expression
expression_1 ? expression_2 : expression_3
is a valid immediate arithmetic expression, which is triggered by a change in any immediate variable in any of the three subexpressions. An alternate form of conditional expression, which leaves out the middle expression is allowed by modern C compilers, particularly by gcc and is allowed in iC (if the C compiler used supports the construct)
expression_1 ? : expression_3
The following excerpt from 'info gcc' explains the advantages and use of the construct:
5.8 Conditionals with Omitted Operands
The middle operand in a conditional expression may be omitted. Then if the first operand is nonzero, its value is the value of the conditional expression.
   Therefore, the expression
     x ? : y
has the value of `x' if that is nonzero; otherwise, the value of `y'.
   This example is perfectly equivalent to
     x ? x : y
In this simple case, the ability to omit the middle operand is not especially useful. When it becomes useful is when the first operand does, or may (if it is a macro argument), contain a side effect. Then repeating the operand in the middle would perform the side effect twice. Omitting the middle operand uses the value already computed without the undesirable effects of recomputing it.
## Parentheses
In immediate C it is possible to write mixed arithmetic and bit expressions, nested to any depth using the usual precedence rules and parentheses.
Immediate arithmetic expressions are evaluated as a whole C expression, every time one of their component immediate variables changes – but only then. To improve execution speed, it is sometimes more efficient to break up very long immediate arithmetic expressions with many operands into several subexpressions – particularly if each subexpression is triggered by different operands. In this case not all the subexpressions are executed. On the other hand there is a certain amount of overhead for triggering each new node and execution of a compiled C expression is fast, even if it has many operands.
Immediate bit expressions are compiled into a network of forward looking nodes, one for each different bit operand and execute even more efficiently. There is no need to break up a complex immediate bit expression into subexpressions – the compiler does this already. Immediate bit expressions embedded in an arithmetic expression are compiled into seperate subexpressions and only the type converted arithmetic result is used in the arithmetic expression.
## Immediate statements
Most immediate statements are immediate declarations or immediate assignments terminated by a semicolon. Immediate declarations and assignments may be combined.
### Immediate declarations
An immediate declaration declares an immediate variable to be either of type imm int or imm bit, using syntax similar to declarations in C. (Declarations of type imm clock and imm timer will be covered later). Any variable not declared before it is used is assumed to be of type imm bit. (Calling the immcc compiler with the strict option -S makes declarations mandatory even for imm bit variables). All variables in a declaration may be assigned to directly.
imm int fader, colourCorrection;	// declarations only
imm int brightness = fader * colourCorrection;
### Immediate Assignments
Immediate assignments are assignments of immediate expressions to immediate variables external to all functions. Value changes to an immediate variable are detected in the assignment and this event triggers the re-calculation of follow on expressions. Like in C, an immediate assignment is also an immediate expression, which means that assignments embedded in expressions are allowed.
### Aliases
Immediate arithmetic and bit assignments, in which the right hand expression consists of only a single immediate variable are accepted by the iC compiler, but produce no code. This type of statement is called an alias. The alias name on the left hand side is simply an alternative name for the immediate variable on the right hand side. Any reference to the alias will be substituted by the right hand side variable, whose value is always the correct immediate value of the intended assignment. Bit aliases may be either normal or inverting. The bit not operator ~ does not produce any code when used on an imm bit operand. All ~x subexpressions are implemented as inverting aliases of x. Thus the direct assignment of ~x to another imm bit variable is also an (inverting) alias.
imm bit a, b;	b = a;	// b is an alias for a (normal)
imm bit x, nx;	nx = ~x;	// nx is an alias for ~x (inverting)
imm int j, k;	k = j;	// k is an alias for j
imm int two;	two = 2;	// two is an alias for 2
### The single assignment rule
Immediate assignments must obey the single assignment rule, a rule which applies generally for data flow systems[1]. Any immediate variable may only be assigned in one immediate assignment. The value of an immediate variable is the value of the expression, from which it is assigned, at all times. A second assignment to the same immediate variable would force different values on that variable, causing a conflict. The immediate variable being assigned cannot hold different values simultaneously. The single assignment rule is monitored by the iC compiler. An error message is generated if it is broken.
[1] see Werner Kluge: The organization of Reduction, Data Flow, and Control Flow Systems - pp. 317. The MIT Press 1992.
Expressions that occur in C code triggered by immediate conditional or immediate switch statements or in C functions in literal blocks may contain immediate variables. These expressions are not immediate expressions and are not triggered by those variables. When such an expression is executed in the C code, the current value of any immediate variable is used.
Immediate variables may even be assigned in C code embedded in immediate conditional and switch statements and in litereal blocks. Such an assignment is not an immediate assignment – the value is changed when the C statement is executed. Nevertheless any change in the immediate variable assigned in the C code will trigger immediate expressions that contain that variable. Several such assignments to the same immediate variable may be made inside different sections of C code. Every new assignment changes the variable in accordance with the intended algorithm. Immediate variables used in C code must be declared as immC bit or immC int in an iC code section. An immediate variable that is assigned in C code may not also be assigned in an immediate assignment.
## Other immediate statements
An immediate conditional statement and an immediate switch statement are the only control constructs available in iC. The syntax of both statement types is similar to their C counterpart, except that braces around the C statements are mandatory. In particular an else if is not allowed, since the if after the else would have been part of the C statement controlled by the else part of the whole immediate if statement, which would be very confusing.
if (imm_bit_expression) { C_statement_1 }
if (imm_bit_expression) { C_statement_1 } else { C_statement_2 }
switch (imm_int_expression) { C_statement }
These are valid immediate statements when they occur external to any function and when the controlling expression is an immediate expression. The controlling expressions in immediate conditional and switch statements are synchronized by a clock. The default clock is iClock. Other clocks or timers may be specified as explained in section 3.12. In all cases any change in the controlling immediate expression, synchronized by the controlling clock, triggers execution of the C statements.
### Immediate conditional statement
For the immediate conditional statement using the keyword if the controlling expression is an immediate bit expression. If not, it is converted from int to bit automatically. A 0 to 1 transition or rising edge causes C_statement_1 to be executed. A 1 to 0 transition or falling edge causes C_statement_2 to be executed (if an else is coded). The C_statements are embedded C compound statements, not immediate statements.
%{
int a, b, c;	/* C declarations in a literal block */
void reset(void);	/* C function declaration */
%}
imm bit sw1, sw2, sw3;	// immediate declarations
if (sw1 & sw2 | sw3) {	/* imm controlling expression */
a = 1; b = 12; c = -2;	/* C code executed on rising edge */
} else {
reset();	/* C code executed on falling edge */
}
### Immediate switch statement
For the immediate switch statement, the controlling expression is an immediate int expression. The C_statement is an embedded compound statement, which has the usual form of a C switch statement with case labels. Any change in the controlling expression triggers the switch statement. The value of that expression after the change is applied to the switch and the selected case is executed.
%{ enum Fuzzy { OFF, DIM, MEDIUM, BRIGHT }; %}	// literal block
switch (brightness) {	// declared and assigned above
case OFF:	lightVoltage(0);	break;
case DIM:	lightVoltage(10);	break;
case MEDIUM:	lightVoltage(18);	break;
case BRIGHT:	lightVoltage(24);	break;
default:	lightVoltage(24);	break;
}	// end of immediate switch statement
The immediate conditional and switch statements open the way to trigger the execution of short C fragments on particular events. These events are either rising or falling edges of bit values or changing arithmetic values. If more than a fragment of C code is involved, it is good practice to code this in a C function, and to call that function in the immediate statement. Very long immediate statements would make the purpose of those statements unclear. Depending on the time critical nature of the application, C code should not take too long to execute, because during the execution of such C-fragments the processing of other immediate events is held up.
## Literal blocks
Literal blocks are sections of C code enclosed in special braces %{ and %}. They may occur before, between and after any immediate statements. Literal blocks are copied verbatim to the front of the generated C output code (without the special braces). Literal blocks are useful to declare any C variables, define macros and to declare and define auxiliary C functions to support the application. Any C-pre-processor statements such as #include or #ifdef must be written as %#include or %#ifdef in the literal block. The %# must be written without intervening spaces. The % is dropped by the iC compiler in copying the literal block to the generated C code. This allows C-pre-processor statements for the iC sections of code which are resolved before the iC compilation.
%{
%#include <math.h>	/* special iC-pre-processor syntax */
int x, y, z;	/* declarations in a literal block */
int abs(int);	/* C function declaration */
%}
The run-time system will call the function iCbegin() when an iC application is started before any immediate processing. This function can be provided by the user in a literal block. If it is not provided, an empty function iCbegin() returning 0 is provided by the system. User implementations should return 1. One use of iCbegin() is to initialise immC variables. It may even contain a fork() call to spawn a child process, which will run in parallel with normal immediate processing. This opens up the way to build mixed applications using conventional multi-process or multi-threaded control strategies in parallel with immediate C code, which leaves a lot of CPU time to do other things.
The complementary function iCend() is called by the run-time system when an iC application is terminated externally (iC applications never terminate by themselves). iCend() could be used to free memory allocated with malloc or new.
%{
int iCbegin()	{ ...; return 1; } /* optional C initialisation */
int iCend()	{ ...; return 1; } /* optional C termination */
%}
If the code in literal blocks, or code in C blocks controlled by an immediate if else or switch, is specifically C++ code, then the generated code must be compiled by a C++ compiler. The Code generated from the iC statements is pure C code.
## Comments
C style comments /* ... */ can be used anywhere between tokens of iC programs.
C++ style comments may be used at the end of iC lines.	// ...
Some older C compilers do not support C++ comments, so their use in literal blocks and C statement blocks controlled by if and switch may lead to portability problems.
## Scope of immediate statements
Immediate variables are global or static and must be declared external to all functions like other global variables in C. Moreover all immediate statements must also be placed external to functions. A statement in a function is only executed (made active) during the execution of that function. Immediate statements are active at all times.
Consecutive immediate statements are not executed in sequence. Each immediate statement is independent of all other immediate statements. They can be placed in any order, without influencing the behaviour of the program. This is analogous to the placement of global variables and functions in C.
Immediate assignments are often combined with their declarations and look like the initialization expressions of ordinary global C variables. In C, this initialization takes place before the function main() is started. In iC, immediate statements simply stay active until the program is stopped. For most of the time the process running the iC program waits in a select() call, which wakes up whenever an external input or internal timer changes. Because the processing required to react to such an input is in the order of microseconds, this strategy ensures that the CPU loading of an iC process is minimal. This can be observed easily with tools like xosview under Linux. Times measured with a modern 1.8 Ghz processor were > 100 µs, which is mostly overhead to get the input process scheduled. The time to even execute a chain of 10 consecutive events is of the order of 10 µs. This corresponds to a 0.1% loading for a process including a 100 ms timer, of which 0.01% is actually used by the immediate statements.
/* VERY SIMPLE WASHING MACHINE PROGRAM */
imm bit on;	// switch to turn system on/off
imm bit waterLo;	// water level switch
imm bit tempLo;	// thermostat, turns off when hot
imm bit fill = on & waterLo;	// fill with water until filled
imm bit heat = on & ~waterLo & tempLo;	// heat water when filled
## Intrinsic limitations of immediate statements
Structures containing immediate variables and arrays of immediate variables have not been realized in the current release, although they are possible and may be implemented in a future release. Pointers to immediate variables in immediate expressions are semantically indeterminate. They are therefore not implemented. This is also pointed out in one of the recommendations in the IEC-1131 standard, which justifies the language 'Structured Text' instead of C on the grounds, that a pointer in a machine control program has no meaning and could cause disaster. The same limitation has been recognized in the language Java, which only recognizes references as constant pointers.
Immediate assignments, in which the left hand side variable appears in the right hand side expression are of very doubtful utility. Such a statement expresses a very tight feedback loop, which will either lock up, or generate a high speed oscillator. For this reason a warning message is generated by the iC compiler.
imm bit a, b;
a = a & b;	// a locks up when b becomes 0
b = ~b | a;	// b oscillates when a is 0
imm int j;
j = j + 1;	// j never catches up with itself
For the above reason the C assignment operators +=, -= etc. as well as ++ and -- cannot be used in immediate statements. Feedback over several statements is allowed, but oscillations are controlled so that the system does not become compute bound. If oscillations do occur, a runtime warning is produced since they are probably not intended.
Like in any programming language, it is possible to write incorrect iC programs. It is the job of the programmer, to understand the model on which the execution of the iC language constructs is based, and to create programs that use these constructs correctly. iC is modelled on hardware building blocks, which provides an easy starting point.
The following was probably intended by the last statement above:
imm bit gate, p;
imm int j;	// j counts every rising edge
if (gate & p) { j++; }	// of p, while gate is hi
In this example, gate & p is an immediate expression that triggers execution of the non-immediate C statement j++; Assignment operators +=, -= etc. as well as ++ and -- with immediate variables are allowed in embedded C statements. The above construct is one way to implement a counters in iC. A better way is shown in section 3.9.
## Pragmas
Pragmas affect the compilation phase of an iC program. Pragmas are introduced by the keywords use or no. use turns an option on; no turns it off. Currently two pragmas are implemented: alias and strict.
use alias;	// equivalent to -A command line option
no alias;	// turn alias option off
use strict;	// equivalent to -S command line option
no strict;	// turn strict option off
The alias pragma or -A option results in aliases to generate a node in the generated C-code (default is to generate no node), which is required if several independent iC sources are to be compiled and linked together and one of these sources refers to an arithmetic (imm int) alias in one source by an extern reference in another source. The use alias option is also useful for debugging, because only when it is set, are alias names displayed as active words by iClive.
The strict pragma or option forces the compiler to expect a declaration of all immediate variables, before assignment. The default with no strict, is to generate an imm bit node for an assignment to an undeclared name. Similarly an assignment to an undeclared name from a CLOCK() or TIMER() function call results in a default imm clock or imm timer variable. Such laxness is OK for small single source projects, but can lead to problems with larger projects. I had a case in a large project, where I had declared a number of imm int variables and mistyped one of them, so the correct name was not declared. This name was then assigned - but converted to imm bit and then back to imm int when used, leading to incorrect arithmetic.
Several options (currently only two) may be set or reset together in one pragma call:
use alias strict;	// equivalent to -AS command line option
no strict alias;	// turn both options off
It is recommended to write use alias strict; as the first line of all production iC programs - the space overhead for extra alias nodes is insignificant and debugging becomes much easier. strict is highly recommended anyway and results in no binary overhead. (Grateful acknowledgements to the designers of PERL).
# Built-in Functions
iC has a number of built in functions, which are so central to the operation of the system, that they have been made a part of the language. They are implemented as efficient building blocks in the supporting run time package. These functions could not all be created from simpler iC statements alone. All except the LATCH and the FORCE functions are 'clocked' which is analogous to similar functionality in hardware IC's.
## Unclocked flip-flop or LATCH
The unclocked R-S flip-flop is the LATCH function with the following calling sequence:
LATCH(set, reset)
The following truth table describes the LATCH function:
set reset | L(set,reset)
        | Q
------------+-------------
0 0 | Q
1 0 | 1
0 1 | 0
1 1 | Q [2]
[2] Note the memory behaviour of a LATCH when both set and reset is 1
The LATCH function is particularly fast and efficient, using only a single gate node. It is of course possible to program a latch function with a pair of cross coupled OR gates. In iC this looks as follows:
imm bit set, reset, Q, Qbar;
Q = set | ~Qbar;
Qbar = reset | ~Q; [3]
[3] Note for PLC programmers: the order of the set and reset statement has no influence on the output of flip flops and latches as it does in sequentially executed PLC programs - even in the case of this latch example using two gates.
The disadvantage of this implementation is the fact that its function as a latch is hidde
        DEBUG optionsn, that two gates are used and that Q and Qbar are both 1, when set and reset are 1 (which means that Qbar should never be used). LATCH clearly shows its function.
## FORCE function
Closely related to the LATCH function is the FORCE function with the following calling sequence:
FORCE(arg1, on, off)
The following truth table describes the FORCE function:
arg1 on off | F(arg1, on, off)
------------------+---------------
0 0 0 | 0
1 0 0 | 1
x 1 0 | 1
x 0 1 | 0
0 1 1 | 0
1 1 1 | 1
The FORCE function passes the value of arg1 to the output if both on and off are 0 (or both are 1). If only on is 1 then the output is forced to 1, independent of the value of arg1. Conversely if only off is 1 then the output is forced to 0. This function is useful for testing.
Note for deep thinkers: the following expression generates a LATCH function from a FORCE function.
(temp001 = FORCE(temp001, set, reset)) [4]
[4] This is how a LATCH is generated by the iC compiler from the more fundamental FORCE function.
## Clocked D flip-flop
The simplest clocked flip-flop is the D flip-flop or delay memory element, a function having a single input, a clock input and an output equal to the input in the previous clock period.
D(expr, c) or D(expr)	/* default iClock used as clock */
The following truth table describes the D flip-flop:
expr | D(expr,c)
D n | Q n+1
--------+----------
0 | 0
1 | 1
The D flip-flop has become the most commonly used clocked flip-flop in hardware design. Its application is called for, when several logic expressions must produce synchronized outputs, so that any further logic done with these outputs does not suffer from timing races. A typical example is the implementation of a state machine. The D flip-flop is also a 1 bit memory element, which can store information from one clock period to the next. The D flip-flop is called for in any design where feedback is involved. The use of the clocked D flip-flop in iC will probably fall into a similar pattern.
Examples of statements using D flip-flops is the generation of a pulse on the rising edge of an input and of a pulse on a change of input.
imm bit input;
imm bit rise = input & ~D(input);
imm bit change = input ^ D(input);
The output 'rise' goes hi when 'input' goes hi and goes lo again when the output of the inverted D flip-flop goes lo after the next (implicit) clock pulse. The second example uses the exclusive-or operator ^ to generate a pulse on both the rising and falling edge of the input.
## Clocked SR flip-flop
The memory element that is represented in most PLC instruction sets is the R-S flip-flop. This flip-flop has two inputs. The rising edge of the set input puts the flip-flop in the "one" state and the rising edge of the reset input puts the flip-flop in the "zero" state. Many books on switching theory describe a simple unclocked latch memory element by the name R-S Flip Flop. Following the usage in IEC-1131, and because the set parameter precedes the reset parameter in the calling sequence, the clocked Set-Reset flip-flop was named SR flip-flop in iC:
SR(set, reset, c)
The following truth table describes the SR flip-flop:
set reset | SR(set,reset,c)
S n R n | Q n+1
----------+----------------
0 0 | Q n
0-1 X | 1
X 0-1 | 0
1 1 | Q n
The SR flip-flop implemented in iC differs marginally from the classical R-S flip-flop described in the literature, which has the disadvantage that Qn+1 is undefined for S and R both "one". The design rules stated that S and R must never be "one" together. Since this would cause unwarranted confusion the implementation with the above truth table was chosen, which gives identical results with designs following the rules of the classical R-S flip-flop. If the rule of both inputs "one" is ignored, the results are still easy to interpret. For the above reasons clocked R-S flip-flops are rare as integrated circuits.
## Clocked SRX flip-flop
In practice the simple clocked SR flip flop can be difficult to control under the following conditions:
A 0-1 set transition has occurred which sets the flip flop and some time later a 0-1 reset transiton occurs which resets it, while set is still a 1. Even if reset goes back to 0, the set input is not active again until it goes back to 0 and then to 1 again. This works well in many situations, but can be counter intuitive for which reason the SRX flip flop or the JK flip can be used more effectively.
SRX(set, reset, c) equivalent to SR(set & ~reset, reset & ~set, c)
The following truth table describes the SRX flip-flop:
set reset | SRX(set,reset,c)
S n R n | Q n+1
----------+----------------
0 0 | Q n
0-1 0 | 1
0 0-1 | 0
1 1 | Q n
1-0 1 | 0
1 1-0 | 1
When both set and reset are 1, then both internal SR inputs are 0. If there is a 1-0 transition on either set or reset, then the alternate input has a 0-1 transition which sets or resets Q.
## Clocked JK flip-flop
Instead J-K flip-flops were made, which toggled their output on every clock pulse, when J and K are both "one". In recent years even these have not been listed in the IC data books. A JK flip-flop has been implemented in iC. :
JK(set, reset, c) equivalent to SR(set & ~Q, reset & Q, c)
The following truth table describes the JK flip-flop:
set reset | JK(set,reset,c)
J n K n | Q n+1
----------+----------------
0 0 | Q n
1 0 | 1
0 1 | 0
1 1 | ~Q n
## D flip-flop with Set and Reset
D flip-flops may have an optional reset input. Another option is to have both a set and reset input as well as the D input. The names of these variants indicate which parameters are required:
DR(expr, reset, c)
DSR(expr, set, reset, c)
For all built in functions, each parameter may have its own clock parameter. If a clock parameter is supplied it applies to all parameters on its left, which do not have their own clock. If no clock parameter is specified, the built in iClock is used.
## Mono-Flop with optional Reset
The Mono-Flop, or SRT() function is a modified SR flip-flop, in which the output is internally connected back to a reset input. This internal reset is usually clocked by a "TIMER" which is controlled by a delay parameter. The delay parameter may have a fixed or variable numeric value. The SRT output is reset, when the number of "TIMER" ticks corresponding to the value of "delay", when the SRT was set, has occurred. An additional optional reset parameter can reset the SRT monoflop prematurely.
SRT(set, timer, delay)
SRT(set, reset, timer, delay)
Instead of clocking with a delay TIMER, any clock may be used. The SRT monoflop is then reset on the next clock pulse after it has been set. When no clock is specified iClock is used, which produces a thin pulse, one clock period wide.
## Sample and Hold
This function is a direct analogy of the clocked D flip-flop for arithmetic values. The arithmetic output equals the arithmetic input in the previous clock period.
SH(arithmeticExpr, c)
The sample and hold function can be used to sample fast changing arithmetic inputs at a constant clock rate. Other uses are the implementation of many useful constructs such as state machines, counters and shift registers, to name a few.
imm int count = SH(count + 1, c);	// count clock c pulses
// shift register with b as input in the least significant bit.
imm bit b;	// b assigned somewhere else
imm int shift = SH((shift << 1) + b, c);
## Sample and Hold with Set and Reset
The Sample and Hold function also comes with either reset or set and reset inputs. When the reset input is clocked, the output is set to all 0's. By analogy when the set input is clocked the output is set to all 1's. The inputs set and reset are imm bit expressions, whereas the main input arithmeticExpr and the output are imm int.
SHR(arithmeticExpr, reset, c)
SHSR(arithmeticExpr, set, reset, c)
## Edge detectors
It is often useful to generate a pulse on the rising edge of a logic signal or on a change of value. These pulses should turn off at the next clock. In connection with the D flip-flop, expressions were shown which generate such pulses. Since these operations are quite important, more efficient functions RISE(expr,c) and CHANGE(expr,c) are implemented in iC. The following statements achieve the same results:
imm bit input;
imm bit rise = RISE(input, c);	// pulse on rising edge
imm bit fall = RISE(~input, c);	// pulse on falling edge
imm bit change = CHANGE(input, c);	// pulse on both edges
The CHANGE function is also implemented for arithmetic expressions.
imm int value;
imm bit arithmeticChange = CHANGE(value, c);
The bit variable arithmeticChange pulses every time value changes, qualified by the clock c. The clock limits the rate at which changes are recognized. This is often useful with numeric values, which may change at a high rate, and a slower sampling rate is called for.
NOTE: there is a significant difference between the output of the RISE function and the output of the SRT monoflop. The output of the RISE function turns on with the rising input signal and turns off again on the first clock. The output of the monoflop turns on with the first clock after the set signal and turns off with the first clock after that, which must be one clock pulse later, assuming the same clock is used for set and internal reset. When the two clocks are different, which is usual for SRT monoflops, the case is different again.
## Clock Signals
There are two types of Clock signal, 'clock' and 'timer'. It is important to realize that Clock signals are not of the same type as logic signals. Clock signals are declared as follows:
imm clock myClock;
imm timer myTimer;
Under no circumstances may clocks be interconnected with logic signals. Any attempt to do so generates an error message. Clock signals in iC are best thought of as timeless pulses, whose occurrence marks the separation of one clock period from the next clock period. All the clocked functions in iC follow the Master-Slave principle. The Master element in a D flip-flop follows the input. The output of this Master gate is transferred to the Slave element during the active phase of the next clock pulse. The output of the Slave element is the output of the D flip-flop. All the Master-Slave transfers during one particular clock pulse are completed before more combinatorial logic or arithmetic expressions are executed. This insures that the outputs of all functions, which are synchronized by the same clock, change simultaneously as far as the logic is concerned.
Clock signals can come from three different sources.
## Built-in immediate clock
There is a built-in immediate clock with the name iClock. This clock runs at the highest system rate. iClock is used as the default clock, when no other clock is specified. It may also be specified by the name iClock when no default clock is allowed by the syntax of a function call.
x = SR(a, b);	// Set and Reset clocked by built-in iClock
y = SR(a, iClock, b, myClock);	// clock for the Set argument
// must be named if different
// from the Reset clock
## CLOCK function
The second source of clock signals is the CLOCK function, which has one or two logic inputs and an optional clock input. The CLOCK function produces an output clock pulse during the active phase of the input clock, which follows a 0 to 1 transition of one of the logic inputs. If no clock input is specified, iClock is used. All CLOCK outputs are synchronous with their input clock.
imm clock clk = CLOCK(b);	// clock on the rising edge of b
// clocked by ‘iClock’
imm bit y = D(a, clk);	// D flip-flop clocked by ‘clk’
iClock|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|
b |~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|
clk __|___|___|___|___|___|___|___|___|___|___|___|___|___
a __|~~~~~~~~~~~~~~~~~~~|_______|~~~~~~~|___|~~~~~~~~~~
y ______|~~~~~~~~~~~~~~~~~~~|_______|~~~~~~~|___|~~~~~~~

imm clock cl2 = CLOCK(b,~b);	// clock on rising and falling edge	// of b, clocked by ‘iClock’

## TIMER function
The third source of clock signals is the TIMER function, which also has one or two logic inputs and an optional clock input. The clock pulses generated by the TIMER function are generated in precisely the same way and at the same time as clock pulses from a CLOCK function with the same inputs. TIMER pulses differ from CLOCK pulses in the way they are used. Clock inputs from a TIMER source must be followed by an arithmetic expression, which may be a constant value. The value of the arithmetic expression is read on the rising edge of the associated logic input, and the result n is used to count timer pulses. The n'th TIMER pulse after the rising input clocks the output. On the falling edge of the logic input the output is clocked immediately by iClock. A TIMER clock used with a D flip-flop produces a function with turn on delay. If the logic input to such a delay element turns off before the delay time is up, the output never turns on. This is a very useful function to implement time-outs, which are notoriously difficult to implement by conventional means.
imm timer tim = TIMER(b);	// timer on the rising edge of b
// clocked by iClock
imm bit z = D(a, tim, 3);// D flip-flop clocked by tim,
// turn on delayed by 3 tim pulses,
// immediate turn off clocked by iClock
iClock|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|_|
b |~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|~|_|
tim __|___|___|___|___|___|___|___|___|___|___|___|___|___
a _|~~~~~~~~~~~~~~~~~~~~|_____|~~~~~~~~~|_|~~~~~~~~~~~~~~~
    <--3 tim--> im <-short-> <--3 tim-->
z ____________|~~~~~~~~~|_____________________________|~~~
Both CLOCK and TIMER functions have optional clock inputs, which come from other CLOCK and TIMER functions. The cascading of these functions allows the realization of many useful applications.
## Built-in Inputs
There are a number of inputs, which have such universal significance, that they are implemented in the run time system.
## iClock
There is a built-in immediate clock with the name iClock. This clock runs at the highest system rate. The name iClock is built-in and may be used as defined above in 3.13.
Because secondary clocks either use iClock by default, or another clock that is eventually clocked by iClock, all clocks (and timers) are synchronous with iClock. The execution of immediate logic is triggered by some input, which causes evaluation of follow up statements, until no more changes occur. iClock generates a clock pulse after every such burst of activity in the logic. iClock has the same significance for immediate logic as the end of the program cycle in a conventional PLC. The main difference is, that for a conventional PLC all statements are executed for each program cycle. For immediate logic only the changes triggered by one or at most a few simultaneous inputs are executed for each program cycle. This typically takes a few microseconds at most for a modern processor. There are support tools which can measure and display this time in microseconds.
## End of Initialization
The rising edge of TX0.0 is guaranteed to be the first input to the system and can be used for initializing user constructs. It is high for the remainder of the program (forever as far as applications are concerned)
TX0.0	EOI, off during initialization, then always on
## Timing inputs
To allow programs to work with real time, the following timing inputs have been provided:
TX0.1	100 microseconds	// requires Kernel with 10000 HZ
TX0.2	1 millisecond	// requires Kernel with 1000 HZ
TX0.3	10 milliseconds	// standard Kernel with 100 HZ
TX0.4	100 milliseconds
TX0.5	1 second
TX0.6	10 seconds
TX0.7	60 seconds or 1 minute
The timing inputs can be used to generate clocks, which are synchronous with real time. For example:
imm clock clk100m = CLOCK(TX0.4);	// every 100 milliseconds
## Inputs and Outputs
Inputs and Outputs are named according to the standard IEC-1131. Inputs start with the letter I, outputs with the letter Q. These are followed by a second letter which defines the type of the input or output. X defines a bit I/O, B a byte I/O, W a 16 bit word I/O and L a 32 bit word I/O variable. The 2 capital letters are followed by a number, which defines the address index of the variable in the I/O field. For bit I/O variables this is followed by a full stop and a number in the range 0 to 7, marking the bit address of the variable in the addressed I/O byte. The maximum address index that can be used depends on the implementation of the driver and the underlying hardware. Addresses in the I/O field may be used for bit, byte, word or long word I/O. If all of these are in the same physical address space, care must be taken not to overlap different types of I/O. In this case 16 and 32 bit word I/O's the byte addresses used must be on a 16 bit word or a 32 bit long word boundary respectively. The iC compiler can generate warnings if I/O fields overlap. In the default case, each size variable is assumed to be in its own address space and the address of each variable is simply in index into each address space.
## Digital inputs
IX0.0	bit 0 of input byte 0 – pre-declared as imm bit
IX0.1	bit 1 of input byte 0
IX0.2	bit 2 of input byte 0
IX0.3	bit 3 of input byte 0
IX0.4	bit 4 of input byte 0
IX0.5	bit 5 of input byte 0
IX0.6	bit 6 of input byte 0
IX0.7	bit 7 of input byte 0
IX1.0	bit 0 of input byte 1
IX1.1	bit 1 of input byte 1
...
## Digital outputs
QX0.0	bit 0 of output byte 0 – pre-declared as imm bit
QX0.1	bit 1 of output byte 0
QX0.2	bit 2 of output byte 0
QX0.3	bit 3 of output byte 0
QX0.4	bit 4 of output byte 0
QX0.5	bit 5 of output byte 0
QX0.6	bit 6 of output byte 0
QX0.7	bit 7 of output byte 0
QX1.0	bit 0 of output byte 1
QX1.1	bit 1 of output byte 1
...
## Analog inputs
IB2	input byte 2 – pre-declared as imm int
IB3	input byte 3
IB4	input byte 4
IB5	input byte 5
IW6	input word 6
IW8	input word 8
...
## Analog outputs
QB2	output byte 2 – pre-declared as imm int
QB3	output byte 3
QB4	output byte 4
QB5	output byte 5
QW6	output word 6
QW8	output word 8
...
The IEC-1131 names above define the physical addresses of inputs and outputs in the I/O field. For more readable applications it is highly recommended, that alternate descriptive names are defined for IEC-1131 inputs and outputs. This would normally be done in a table of alias assignments at the start of an iC program. One advantage of this scheme is, that if an input or output is physically moved to another I/O pin, only 1 statement in the source needs to be changed.
imm bit	waterLo, motorOn, heaterOn;
imm int	waterTemp, motorSpeed;
waterLo	= IX1.3;	// these statements define aliases
waterTemp	= IB2;	// which produce no run-time overhead
QX10.2	= motorOn;	// here the IEC-1131 names
QX10.3	= heaterOn;	// are the aliases, which
QW8	= motorSpeed;	// works for outputs
IEC-1131 I/O variable names are pre-declared as immediate variables in iC program code, but they are not defined in embedded C code. Only variables declared with an imm bit or imm int statement are defined in C code. If I/O variables must be accessed in C code the alternate names must be used. This is another reason for defining descriptive aliases for I/O variables.
# User defined immediate Function Blocks
User defined immediate functions are commonly called function blocks in the PLC world, because they act more like functional blocks or templates rather than functions in the instruction flow sense, where a function evaluates a sequence of instructions whenever it is called. An immediate Function Block is a separate immediate subsystem with immediate parameters which are its inputs and outputs from other section of the immediate system, optional internal immediate variables, which must be declared inside the Function Block and an optional immediate return value, which may be used like any other immediate value – in an expression – assigned to an immediate variable or used as an input parameter in a built in function or function block call. Only standard IEC-1131 I/O variables may be used in a Function Block without being declared, although they may only be used as inputs, since any assignment to an I/O variable such as QX0.0 inside a Function Block would lead to a multiple assignment, once the Function Block is used more than once. Another way to look at an immediate Function Block is like a higher level integrated circuit, which has connections into the system and provides a certain complex function with many internal components and connections.
## immediate Function Block Definition
An immediate Function Block must be defined before it is used. Since the definition of a Function Block does not itself generate any C-Code on compilation it can be and usually is defined with its code body in a header file, if multiple source files are used for a project. For small projects with a single source file Function Blocks can be defined at the start of the source file.
immediate Function Blocks definitions are very similar to C-functions, although there are significant differences in detail. The definition of an immediate Function Block consists of a return value type, a Function Block name, a comma separated parameter list in parentheses and a function body in curly braces, e.g.
imm bit fall(bit f, clock c) { this = RISE(~f, c); }
The return value may be one of 5 types:
imm void	// which means no value is returned
imm bit
imm int
imm clock
imm timer
The imm modifier is mandatory for the return type – it identifies an immediate Function Block Definition syntactically. The Function Block name can be any valid name starting with a letter followed by any number of alphanumeric characters or underscores. A leading underscore is possible, but should be avoided. The name must be distinct from all other immediate variable names in a project.
The individual formal parameters in the parameter list must be of the following 4 types:
imm bit	// or simply	bit
imm int	// or simply	int
imm clock	// or simply	clock
imm timer	// or simply	timer
The imm modifier is optional for parameters in the parameter list. The variable declared is nevertheless immediate. Parameters may be either input value parameters, in which case only their type is written in the list or the parameter may be an immediate output to which a value from the Function Block is to be assigned. In this case the type of the parameter must be preceded by the keyword assign.
The body of a Function Block is one or more immediate statements defining the functionality of the block encoded in curly braces. Immediate variables internal to the function must be declared before use in the Function Block. Parameter names and internal variable names are in a separate name space for each function, which is also separate form the global name space. If a Function Block is not imm void the body must contain a return statement. The semantics of the return statement is the assignment to the variable to which the Function Block is assigned, when it is called. This variable, which is identified by the keyword this, may be used in other expressions inside the Function Block. The preferred way to write the retun statements is:
this = some + immediate + expression;	// preferred return syntax
The usual C-syntax may also be used, but does not make the action as clear:
return some + immediate + expression;	// deprecated earlier syntax
The return statement need not be the last statement in the Function Block definition – its position does not influence when it is executed – that is controlled purely by changes in the values of the variables making up the return statment – something which holds for all immediate statements. This situation is more clearly expressed by the assigment to this. An imm void Function Block has no this variable, may not contain a return statement and may not be assigned when called.
Each assign parameter must be on the left side of an assignment statement in the Function Block. The values of assign parameters may be used inside the Function Block. Each variable declared inside the Function Block must also be assigned in the Function Block. Variables declared extern outside or inside the Function Block may not be assigned to inside the Function Block. As is the case with I-O variables (which are implicitly extern) extern variables may only be used as values inside the Function Block. They may not be declared again as local inside the Function Block. Variables declared extern in a function may be declared after the definition of the Function Block in the iC code following the definition, to declare that the variable will be assigned in this module. A variable with the same name as an extern variable may be declared locally in another Function Block, but it is a different formal variable local to that Function Block.
All immediate statement types – assignments, if else, switch, Built in Functions and other user defined Function Block calls may be used in Function Blocks definitions. Function Blocks may be nested to any depth as long as Function Blocks are used, which have been previously defined. This implies that Function Blocks cannot be called recursively, either directly or indirectly. Function Blocks may be very simple one line definitions or complex systems with hundreds of parameters. Several examples follow:
The SRX flip flop is built into the compiler, but defined in just this way during initialisation of the compiler. In the latest version of the compiler, all but the most primitive built ins, are defined as Function Blocks.
/* SRX flip flop defined as a function block */
imm bit srx(imm bit set, imm clock scl,
 imm bit res, imm clock rcl)
{
this = SR(set & ~res, scl, ~set & res, rcl;
}
The CountClk function adds 'increment' to 'this' for every occurrence of 'clk':
imm int CountClk(imm clock clk, imm int increment)
{
this = SH(this + increment, clk);
}
The CountBit function adds 'increment' to 'this' for every rising edge of 'step':
imm int CountBit(imm bit step, imm int increment)
{
this = CountClk(CLOCK(step), increment); // nested call
}
The SelectClk function selects either a 100 ms or a 1 second clock with variable 'second':
imm clock SelectClk(imm bit second)
{
this = CLOCK(TX0.4 & ~second |	// 100 ms
  TX0.5 & second );	// 1 second
}
The following function block ADConvert assigns the conversion of int val to 8 assign bit variables b0 to b7 passed as parameters (imm is implied for value and assign parameters).
/* Analog to digital conversion of a byte value */
imm void ADConvert(int val,	// input parameter
assign bit b0,	// output parameters
assign bit b1,
assign bit b2,
assign bit b3,
assign bit b4,
assign bit b5,
assign bit b6,
assign bit b7,
)
{
b0 = val & (1 << 0);	// assignments to outputs
b1 = val & (1 << 1);
b2 = val & (1 << 2);
b3 = val & (1 << 3);
b4 = val & (1 << 4);
b5 = val & (1 << 5);
b6 = val & (1 << 6);
b7 = val & (1 << 7);
}
Note: the parameter list may have a trailing comma before the closing parentheses. This is generally the case for comma separated lists in iC and makes it easier to edit the lists and copy parameters when written vertically, which is useful for large parameter lists.
The iC compiler builds a template of the Function Block, replacing each parameter and internally declared variable by the name of the Function Block followed by a '@' and the formal parameter or declared variable name. This strategy ensures a private name space for each Function Block. When called, the template is copied, with each formal parameter replaced by its real parameter and internally declared variables replaced by the formal name with the '@' replaced by an underscore '_' and followed by an underscore and an instance number. The instance number scheme ensures that there is no clash of compiler generated variable names (even for seperately compiled modules).
## immediate Function Block Call
An immediate Function Block is called in a similar fashion to a C-function, again with some significant differences. In practice immediate Function Blocks are not called. When the compiler encounters a Function Block call, the pre-compiled Function Block, which is like a template, is copied, with all parameters replacing the formal parameters in the template. The resulting network of nodes will then be used at run-time like the network of nodes produced from all other immediate statements.
If an imm void function is encountered it looks like a subroutine call:
ADConvert(IB1,
QX0.0, QX0.1, QX0.2, QX0.3,
QX0.4, QX0.5, QX0.6, QX0.7,
    );
This statement will assign bits 0 to 7 of IB1 to QX0.0 to QX0.7 whenever IB1 changes.
A Function Block with a return value must either be assigned to a suitable variable or else it must be used as a value of a suitable type in an expression or in a parameter list. An imm bit Function Block may be used as an imm int value and vice versa – appropriate conversion takes place. imm clock and imm timer Function Blocks can either be assigned to correctly declared clock or timer variables or else used as a clock or timer value in a parameter list.
/* count every rise of IX1.0 */
imm int count = CountBit(IX1.0, 1);
/* selects 1 sec when IX1.7 is on else 100 ms */
imm clock clk = SelectClk(IX1.7);
Real parameters of type imm int and imm bit may be mismatched with their formal parameter types – value and assign parameters in the call will be forced to their formal type. assign parameters of type imm clock and imm timer must match – so must a value parameter of type imm timer. The handling if formal imm clock parameters is more complex, allowing the use of default clocks.
Positions for formal imm clock parameters are handled as follows:
1. the position may be filled by a real imm clock parameter.
2. the position may be filled by a real imm timer parameter followed by an optional imm int delay (if delay is left out it will be set to 1).
3. the position may be left out altogether, in which case the next clock or timer parameter on the right will be replicated for the position. If there is no real clock parameter following on the right, iClock will be used.
Real timer parameters for formal timer parameters cannot be extended by a delay – the delay used is determined in the Function Block with delay(s) associated with the use of the formal timer parameter in the code of the Function Block.
The following calls of the user defined srx() Function Block (which is identical to the built in SRX) with two formal clock parameters – one each for set and reset.
imm clock c = CLOCK(IX1.1), clk = CLOCK(IX1.2);
imm timer t = TIMER(IX1.3);
imm bit s, r;
imm bit m1 = srx(s, clk, r, c);	// uses individual clocks
imm bit m2 = srx(s, t, 3, r, t, 5);	// individual timer delays
imm bit m3 = srx(s, r, clk);	// one clock for s and r
imm bit m4 = srx(s, r, t, 5);	// one timer for s and r
imm bit m5 = srx(s, clk, r);	// default iClock for r
imm bit m6 = srx(s, iClock, r, c);	// must specify iClock here
imm bit m7 = srx(s, r);	// default iClock for both
The following example is a controller for a full scale application which required all the space and speed resources of a PLC in the mid 80's. This project for a parcel sorting system for the Australian Railways prompted the author to look at alternate event driven systems for machine control.
The program is meant to control 4 high speed belts moving at 5 metres/second generating independent strobe pulses for every 15 mm movement of the belt. That means a strobe pulse every 3 ms. Each belt is equipped with 32 destination gates spaced 12 strobe pulse apart and open for 7 strobe pulses (in practice this must be 72 strobe pulses or more).
The implementation consists of several function blocks:
feeder() controls the insertion of the destination code onto the initial feeder segment of the belt.
segment() controls one of the 32 identical segments of the belt.
belt() is a Function Block for one belt, calling feeder() once and segment() 32 times.
Finally belt() is called 4 times – once for each belt.
tick() is an auxiliary Function Block generating strobe pulses for the simulation.
Note the way tick() is called in the strobe parameter position of belt().
The compiled program is 96 Kbytes in size consisting of 1944 Gate nodes, 8642 links and 10 C functions consisting of 1 line of C code each.
/********************************************************************
*
*	Parcel sorter for long belts
*	Author:	J.E. Wulff
*	Source: Test8/sorti.ic
*
*******************************************************************/
/********************************************************************
*
*	Feeder segment
*
*******************************************************************/
imm bit feeder(	/* feeds code into feeder segment */
imm bit transfer,	/* photo cell to transfer code */
assign	imm int carryOut,	/* shift bit (as int) for the following segment */
imm int code,	/* destination code - 0 to 31 */
imm int length,	/* sets the length of the segment */
imm int width,	/* width of lock frame 6 + 6 for 0x7f */
imm clock c,	/* stepping clock for the belt */
   )
{
   extern imm bit reset;	/* general re-initialisation */
   imm bit pip = RISE(transfer & ~this & ~reset, c);
   imm int shift = SHR((shift << 1) + (pip * (0x41 + (code << 1))), c, reset);
   imm int mask = 0x41 << width;
   carryOut = (shift >> length) & 0x00000001;
   this = SRX(pip,	/* unlock after width steps */
      (shift & mask) == mask | reset, c);
}
/********************************************************************
*
*	Segment
*
*	Each segment controls one gate and may be up to 32 steps long
*
*******************************************************************/
imm bit segment(	/* returns gate control output */
imm int carryIn,	/* shift bit (as int) from the previous segment */
assign	imm int carryOut,	/* shift bit (as int) for the following segment */
imm int code,	/* code identifying this segment */
imm int length,	/* segment length */
imm int width,	/* width of the gate */
imm clock c,	/* stepping clock for the belt */
   )
{
   extern imm bit reset;	/* general re-initialisation */
   imm int shift = SHR((shift << 1) + carryIn, c, reset);
   imm int mask = 0x41 << width;
   carryOut = (shift >> length) & 0x00000001;
   this = SRX((shift & 0x7f) == 0x41 + (code << 1),
      (shift & mask) == mask | reset, c);
}
/********************************************************************
*
*	Belt
*
*	Each belt has 32 gates
*
*******************************************************************/
imm int belt(
   assign	imm bit lock,	/* lock indicator */
   assign	imm bit gate00,
   assign	imm bit gate01,
   assign	imm bit gate02,
   assign	imm bit gate03,
   assign	imm bit gate04,
   assign	imm bit gate05,
   assign	imm bit gate06,
   assign	imm bit gate07,
   assign	imm bit gate08,
   assign	imm bit gate09,
   assign	imm bit gate10,
   assign	imm bit gate11,
   assign	imm bit gate12,
   assign	imm bit gate13,
   assign	imm bit gate14,
   assign	imm bit gate15,
   assign	imm bit gate16,
   assign	imm bit gate17,
   assign	imm bit gate18,
   assign	imm bit gate19,
   assign	imm bit gate20,
   assign	imm bit gate21,
   assign	imm bit gate22,
   assign	imm bit gate23,
   assign	imm bit gate24,
   assign	imm bit gate25,
   assign	imm bit gate26,
   assign	imm bit gate27,
   assign	imm bit gate28,
   assign	imm bit gate29,
   assign	imm bit gate30,
   assign	imm bit gate31,
imm int code,	/* gate code 0 to 31 for parcel destination */
imm bit p_cell,	/* photo cell monitoring parcel onto belt */
imm bit strobe,	/* strobe pulse from belt movement */
   )
{
   imm int carfd;	/* carry bits */
   imm int car00, car01, car02, car03, car04, car05, car06, car07;
   imm int car08, car09, car10, car11, car12, car13, car14, car15;
   imm int car16, car17, car18, car19, car20, car21, car22, car23;
   imm int car24, car25, car26, car27, car28, car29, car30, car31;
   imm clock clk = CLOCK(strobe);
   lock = feeder(p_cell, carfd, code, 12, 11, clk);
   gate00 = segment(carfd, car00, 0, 12, 7, clk);
   gate01 = segment(car00, car01, 1, 12, 7, clk);
   gate02 = segment(car01, car02, 2, 12, 7, clk);
   gate03 = segment(car02, car03, 3, 12, 7, clk);
   gate04 = segment(car03, car04, 4, 12, 7, clk);
   gate05 = segment(car04, car05, 5, 12, 7, clk);
   gate06 = segment(car05, car06, 6, 12, 7, clk);
   gate07 = segment(car06, car07, 7, 12, 7, clk);
   gate08 = segment(car07, car08, 8, 12, 7, clk);
   gate09 = segment(car08, car09, 9, 12, 7, clk);
   gate10 = segment(car09, car10, 10, 12, 7, clk);
   gate11 = segment(car10, car11, 11, 12, 7, clk);
   gate12 = segment(car11, car12, 12, 12, 7, clk);
   gate13 = segment(car12, car13, 13, 12, 7, clk);
   gate14 = segment(car13, car14, 14, 12, 7, clk);
   gate15 = segment(car14, car15, 15, 12, 7, clk);
   gate16 = segment(car15, car16, 16, 12, 7, clk);
   gate17 = segment(car16, car17, 17, 12, 7, clk);
   gate18 = segment(car17, car18, 18, 12, 7, clk);
   gate19 = segment(car18, car19, 19, 12, 7, clk);
   gate20 = segment(car19, car20, 20, 12, 7, clk);
   gate21 = segment(car20, car21, 21, 12, 7, clk);
   gate22 = segment(car21, car22, 22, 12, 7, clk);
   gate23 = segment(car22, car23, 23, 12, 7, clk);
   gate24 = segment(car23, car24, 24, 12, 7, clk);
   gate25 = segment(car24, car25, 25, 12, 7, clk);
   gate26 = segment(car25, car26, 26, 12, 7, clk);
   gate27 = segment(car26, car27, 27, 12, 7, clk);
   gate28 = segment(car27, car28, 28, 12, 7, clk);
   gate29 = segment(car28, car29, 29, 12, 7, clk);
   gate30 = segment(car29, car30, 30, 12, 7, clk);
   gate31 = segment(car30, car31, 31, 12, 7, clk);
   this = car31;	/* allows concatenation of belts */
}
/********************************************************************
*
*	Generate tick
*	input fast1 or fast2 cause 50 ms ticks
*	else tick for every change of manual input
*
*******************************************************************/
imm bit tick(bit manual, bit fast1, bit fast2) {
   imm bit fast = fast1 | fast2;
   this = CHANGE(manual & ~fast | TX0.4 & fast);
}
/********************************************************************
*
*	4 belts
*
*	Each belt has 32 gates
*
*******************************************************************/
imm bit reset = IX0.7;	/* general re-initialisation */
QX8.0 = belt(
   QX8.1,	/* lock indicator */
   QX0.0, QX0.1, QX0.2, QX0.3, QX0.4, QX0.5, QX0.6, QX0.7,
   QX1.0, QX1.1, QX1.2, QX1.3, QX1.4, QX1.5, QX1.6, QX1.7,
   QX2.0, QX2.1, QX2.2, QX2.3, QX2.4, QX2.5, QX2.6, QX2.7,
   QX3.0, QX3.1, QX3.2, QX3.3, QX3.4, QX3.5, QX3.6, QX3.7,
   IB3,	/* gate code 0 to 31 for parcel destination */
   IX0.1,	/* photo cell monitoring parcel onto belt */
   tick(IX0.0, IX0.6, IX0.5), /* strobe pulse from belt movement */
);
QX8.2 = belt(
   QX8.3,	/* lock indicator */
   QX4.0, QX4.1, QX4.2, QX4.3, QX4.4, QX4.5, QX4.6, QX4.7,
   QX5.0, QX5.1, QX5.2, QX5.3, QX5.4, QX5.5, QX5.6, QX5.7,
   QX6.0, QX6.1, QX6.2, QX6.3, QX6.4, QX6.5, QX6.6, QX6.7,
   QX7.0, QX7.1, QX7.2, QX7.3, QX7.4, QX7.5, QX7.6, QX7.7,
   IB7,	/* gate code 0 to 31 for parcel destination */
   IX4.1,	/* photo cell monitoring parcel onto belt */
   tick(IX4.0, IX4.6, IX0.5), /* strobe pulse from belt movement */
);
QX8.4 = belt(
   QX8.5,	/* lock indicator */
   QX10.0, QX10.1, QX10.2, QX10.3, QX10.4, QX10.5, QX10.6, QX10.7,
   QX11.0, QX11.1, QX11.2, QX11.3, QX11.4, QX11.5, QX11.6, QX11.7,
   QX12.0, QX12.1, QX12.2, QX12.3, QX12.4, QX12.5, QX12.6, QX12.7,
   QX13.0, QX13.1, QX13.2, QX13.3, QX13.4, QX13.5, QX13.6, QX13.7,
   IB13,	/* gate code 0 to 31 for parcel destination */
   IX10.1,	/* photo cell monitoring parcel onto belt */
   tick(IX10.0, IX10.6, IX0.5), /* strobe pulse from belt movement */
);
QX8.6 = belt(
   QX8.7,	/* lock indicator */
   QX14.0, QX14.1, QX14.2, QX14.3, QX14.4, QX14.5, QX14.6, QX14.7,
   QX15.0, QX15.1, QX15.2, QX15.3, QX15.4, QX15.5, QX15.6, QX15.7,
   QX16.0, QX16.1, QX16.2, QX16.3, QX16.4, QX16.5, QX16.6, QX16.7,
   QX17.0, QX17.1, QX17.2, QX17.3, QX17.4, QX17.5, QX17.6, QX17.7,
   IB17,	/* gate code 0 to 31 for parcel destination */
   IX14.1,	/* photo cell monitoring parcel onto belt */
   tick(IX14.0, IX14.6, IX0.5), /* strobe pulse from belt movement */
);
The following are the 10 generated C code fragments. The macro iC_MV accesses an indexed value on the generated link array. One can see from this that even for int nodes the execution time for one event is going to be no more than a few microseconds.

000	(1)	return iC_MV(1)?iC_MV(2):iC_MV(3);
026	(3)	return (iC_MV(1)<<1)+(iC_MV(2)*(0x41+(iC_MV(3)<<1)));
027	(4)	return 0x41<<iC_MV(1);
028	(5)	return (iC_MV(1)>>iC_MV(2))&1;
030	(6)	return (iC_MV(1)&iC_MV(2))==iC_MV(2);
051	(7)	return (iC_MV(1)<<1)+iC_MV(2);
052	(8)	return 0x41<<iC_MV(1);
053	(9)	return (iC_MV(1)>>iC_MV(2))&1;
055	(10)	return (iC_MV(1)&iC_MV(2))==iC_MV(2);
055	(11)	return (iC_MV(1)&0x7f)==0x41+(iC_MV(2)<<1);
# Compiler and Run-time system
## Compiler
The iC compiler immcc generates C code with the extension .c from iC source files with the extension .ic, which is suggested for iC sources. It is also suggested, that iC header files have the extension .ih For larger projects, several .ic files may be compiled to .c files, which are then compiled by cc to .o files and linked with the library libict.a, which contains the run-time code. This produces a finished application, which can be run in an environment compatible with the features of the run-time library.
## Run-time libraries
There are several versions of the run time library, depending on the hardware interfaces available for Input and Output. The Demonstration library libict.a communicates its Input and Output via TCP/IP, which provides a turnaround time of an input change to the arrival of the corresponding output change in a lightly loaded network of less than 2 millisecond (measured on a Pentium 166). The uncertainty of load occurring in such a network forces one to look at specialized bus systems for high speed applications. Currently libict.a is a static library. For production purposes a dynamic library is envisaged.
Other libraries have been built for industrial field bus systems. The library for InterBus-S is complete and has been extensively tested with InterBus-S I/O modules. A library for a proprietary high speed field bus system was used for early tests and provided turnaround times of under a 100 microseconds on a 386 8 MHz processor. A CAN-Bus library is planned and could be implemented at short notice.
## Run-time environment and system
For any applications where hard real time constraints are not a problem, the TCP/IP run-time system provides a very flexible and easy to configure environment where Input and Output may be distributed over a number of computers in a local area network. The system consists of a server called iCserver and a number of clients for which iCserver is the hub. An iC application linked with the libict.a library is one type of client, providing control in the system. The other client types are Input and Output modules (or combined I/O modules) and debugging tools.
The iCserver has been implemented in Perl, which is very flexible and fast enough to keep up with traffic generated in a local area network. A faster C implementation of iCserver is possible. The program iCbox simulates Input/Output modules as Perl/Tk dialog boxes for digital and analog inputs and outputs. For real inputs and outputs iCbox can serve as a program template. Only the translation of the I/O signals to a short network message for transmission to the iCserver is necessary to port an I/O device. A simple and very compact protocol for passing messages to and from the iCserver has been defined.
The program iClive provides an IDE for editing and debugging iC programs. It provides an edit window, in which program text can be displayed and optionally edited, searched, saved, made into runnable code, run and stopped. When running and debugging an iC program, iClive is a client of iCserver and indirectly of the running iC program. iClive colours words in the program text according to the state of the node named by a word – green/black for bit 0, yellow/red for bit 1 and blue for arithmetic words. The value of a node is also displayed when the cursor is on a word. To be effective, the displayed text must be either the source of the running iC program or a text derived from that source, such as the compiler generated listing, which shows all compiler generated extra nodes. With this colour coded display of the statements of the iC program, it is easy to follow the progress of execution and the related logic at run time. "Live displays" are commonly used in programming units for PLC's in industrial control environments to provide debugging support.

Fig. 1	iCbox as IO for “sorti” - IX0.0, QX0.2 and QX8.1 are “on” - the rest are “off”.

Fig. 2	iClive in LIVE mode - QX8.1, QX0.2 and IX0.0 are “on” - the rest are “off”.
“sorti” is running. – it can be stopped by pressing the “Stop” button or switched
to Edit mode by pressing the “Edit” button (see Fig. 3).

Fig. 3	iClive in EDIT mode with a search for IX0.5 shown. The application “sorti” is not running – press “Run” and then “Live” to get to Fig. 2. “Help” to get the following:

Fig. 4	iCman showing the start of the man-page for iClive. A search for “Text” is shown.

For command line use, a shell script iCmake builds one or more applications from iC sources using the static library libict.a. The compiler immcc, the programs iCserver, iCbox, iClive and iCmake as well as each compiled and linked iC application provide a generous help output with the switch option -h. Each of these programs also has a full man page which may be viewed with 'man' in a Unix like environment or with iCman, a man page viewer with interesting search and hyperlink features.
# The Author
John E. Wulff studied Electrical Engineering at the University of New South Wales in Sydney, Australia. His first professional experience was in the Telephone industry, developing switching circuits with electro-mechanical relays but also with vacuum tubes, cold cathode tubes and very soon with the emerging transistors. In 1964 he spent 6 months in England, getting know-how on a new family of switching circuits using germanium diodes and transistors, but which already supported clocked flip flops. These had been developed at the BICC research laboratory near Hampton Court, where John Sparkes had invented the principle of clocking a few years earlier. With this experience, he was chief designer for a special purpose computer with 100 Kbytes of magnetic drum memory, 1 million transistors, 2.5 million diodes for logic and 100,000 silicon controlled rectifiers for power output drivers, switching up to 5 Amps. This machine controlled a letter sorting system with 150 input consoles and a throughput of 5 million letters a day. This system worked reliably for 25 years.
Experience with logic design based on integrated circuits followed. The availability of mini computers led to an interest in programming. A Master of Engineering Science Degree in Information Science at the University of New South Wales provided a solid foundation for future work as a Software Engineer. The design and implementation of a Real Time Operating System, which provided a context switch in 15 machine instructions was the content of his Masters Thesis, and later provided the basis for some very fast machine control systems for industrial control.
In the mid 80's John Wulff came in contact with PLC's. He was asked to help during the commissioning of a PLC-system, controlling a parcel sorting complex consisting of 100 standard conveyor systems and 4 high speed conveyors which had mechanical gates along its length, to divert parcels. These high speed belts needed a control resolution of 15 milliseconds, in which time a parcel had moved 3 cm. Unfortunately the function blocks for the standard conveyors, executed 100 times, once for each of the conveyors, brought the total cycle time to over 1 second!! What to do? Fortunately the PLC had just enough (8) interrupt inputs, to allow the implementation of an event driven sub-system based on the assembler instruction set of the PLC. This saved the company a lot of liquidated damages.
This experience spawned the idea for an event driven PLC, which resulted in the current iC system. Although this system is demonstrably faster than a PLC with the same memory speed for any reasonable application one can think of, it is difficult to compute a guaranteed maximum response time. Since this is a requirement for hard real time applications, iC was never accepted for industrial use. For a PLC the maximum response time is simply the time to execute all instructions making up the program, which is the cycle time of the program. For an iC program this time can also be computed. For a 10 MHz PC the execution time is about 2 microseconds per gate node processed. The total number of gate nodes is provided in the listing produced by the compiler. An iC program with 10.000 gate nodes, which corresponds to a PLC program of approx. 32 Kbytes would thus have a maximum response time of 20 milliseconds, if all nodes were somehow fired simultaneously. This would be a good response time for a PLC. In practice this can never happen and a maximum response times of < 200 microseconds was measured on such a machine. This corresponds to events which cause 100 follow up nodes to fire. The typical number of follow up events is 7. Assuming this figure is Poisson distributed the above assumption is not unreasonable.
Current plans are, to publish the complete system under an Open Source License and to see if the Open Source Community can make a go of it. With the current emphasis on Linux in embedded Systems, I see great scope here.

Id: iC.odt 1.19 2008/02/26